## Slide 1: Take The Cue
Autonomous pool playing robot

## Slide 2: Our Team
Hardware Team
  Guy and Ernest
Electrical and Controls Team
  Andrew and Derek
Software Team
  Eric and Max

## Slide 3: Everyone needs a pool partner!
Most existing solutions are prototypes
  Too expensive
  Too complex to operate
Our solution allows pool players to enjoy their table at all times
Customizable to many table sizes
Easy-To-Use Android module for Visual Recognition
Cost effective ( < $750 )

## Slide 4: Project Summary
Autonomous solution for a pool playing partner
Visual Recognition to make its own decisions
Renders image and detects location of balls
Runs simulation to find best shot
Moves actuator to strike the white ball

## Slide 5: Hardware Summary
X Rail
End Effector/Actuator
Y Rail
X Rails work synchronously
Y Rail is as low as possible
Actuator Strikes ball with varying force
3 motions combine to align Actuator
  X, Y and θ
Arm Base

## Slide 6: Rotating Mechanism
Uses NEMA 17 to preform motion
Gear Ratio => 4:1
Uses encoder to detect orientation
Rides two rails for stability
Rotating Mechanism

## Slide 7: Hardware Hurdles
Hit balls while still moving around easily
  Actuator tilted 20 degrees
Reaching the whole table
  Move rails further out
Strike a ball with sufficient force
  Electrical Motor or Pneumatics
Actuator

## Slide 8: Hardware Demo – Shooting Mechanism

## Slide 9: Hardware Demo – X Rails

## Slide 10: Electrical and Controls Summary
RAMPS 1.4 simplifies design with modular motor drivers
Buttons/endstops for controlling motors within bounds
White line sensors for keeping track of rotational position

## Slide 11: Electrical and Controls Hurdles
One X-rail motor lags behind the other
  Solution: control both motors from the same motor driver
Finding number of steps the motors can traverse along x and y axis
  Solution: write program that counts steps and moves system from one end of the table to the other and stops when button/endstop is triggered
User not knowing the current mode the system is in
  Solution: colour changing LED changes colours according to mode of the system

## Slide 12: Software Summary
Arduino program:
  Receives user commands
  Monitors sensor signals
  Controls motors
  Serial communication with PC
Android program:
  Automated image capture
  Socket communication with PC

## Slide 13: Software Summary (cont.)
Java program:
  Various communication
  protocols with other programs
  Simulates shots to find the
  optimal one
Matlab program:
  Object detection
  Ball identification

## Slide 14: Software Hurdles
Object detection and identification
Relation of simulation to real worlds
Android emulator crashing often
Android uncooperative with
automated image capture

## Slide 15: Software Demo

## Slide 16: Thank You For Your Time!